## Slide 1
Where “Lean” principles are considered common sense and are implemented with a passion!
Product Training
Lean Manufacturing

## Slide 2
Lean Defined
Earlier we defined lean as:
A “visual” factory where demand drives production creating a “pull” system. That is only things that are required are made or purchased. Cells, kanbans, TQM and continuous improvement, identifying and eliminating waste, and visual signals are things generally associated with lean. Lean is as much a discipline as a process.
At WinMan, we believe that “lean thinking” goes beyond the plant floor. It should extend through the entire supply chain and encompass all of your internal functions, including sales, marketing, accounting, etc. Functions such as automatically generating vouchers upon receipt of materials is an example of a lean process as opposed to doing the traditional three way match (voucher, purchase order, receiver). Of course to get there you need to have a trusting partnership with your supplier.

## Slide 3
Lean Partnerships
Partnerships with suppliers is key to leaning out inventories, cutting engineering costs, and decreasing costs. This runs counter to having many suppliers for each item as is the general rule in some industries. The US Auto Industry for instance, demanded price reductions from their suppliers without regard to their suppliers cost or efficiency. A good supplier may have already cut their costs through good management, but they were still required to cut more, often sacrificing quality. Bottom line, good suppliers were punished and bad suppliers rewarded because they had room to but.
In today’s environment, many suppliers have more knowledge about the items they sell to us than we do. Using their R&D to better your parts and reduce their costs (and yours) can save both sides cost. Companies that partner with suppliers this way will often find they have over engineered the part or are creating a part that with a few simple changes could be made at less cost. It is in both parties interest to have both entities being profitable and thriving.
Adversarial relationships do not lead to mutual success.

## Slide 4
Starting the Lean Journey
The main tenant of lean is to drive out waste. Adopting lean techniques helps to identify the waste where as traditional manufacturing will often hide waste.
For companies starting out on lean for the first time, the beginning step is “Value Stream Mapping”. The value stream map starts at the end with the customer and we work our way towards receiving. There are many books and seminars given on Value Stream Mapping.
The value stream map reveals the following:
Product Flow
Where one piece flow ends
Cycle Time
Actual value add time
Waste
Poor information flow
The typical result is the realization that little time is spent on value added activities when compared to the entire cycle time.

## Slide 5
Value Added
Value Added activities are those activities for which a customer will pay.
Take an everyday example of an oil change at an auto shop.
Here is a quick rundown of the activities.
Go get car
Search for the keys
Drive car to work center
Go to tool bin to get wrench that fits oil pan drain plug
Remove drain plug
Let oil drain into used oil receptacle
Go to tool bin to get filter wrench
Remove filter
Dispose of filter
Replace drain plug
Go to parts department to get new filter
Talk to pretty girl at the counter
Replace Filter
Replace Oil
Record work
Drive car to completed work area
Deliver paperwork to cashier

## Slide 6
Value Added
Go get car
Search for the keys
Drive car to work center
Go to tool bin to get wrench that fits oil pan drain plug
Remove drain plug
Let oil drain into used oil receptacle
Go to tool bin to get filter wrench
Remove filter
Dispose of filter
Replace drain plug
Go to parts department to get new filter
Talk to pretty girl at the counter
Replace Filter
Replace Oil
Record work
Drive car to completed work area
Deliver paperwork to cashier

## Slide 7
Non Value Added but Necessary
Some work is non value added but necessary. Inspection falls under that category. In most cases, quality should be built in, thus requiring no or little inspection. However, we would like to make sure that the oil pan drain plug was put in properly. We certainly are happy airplanes are inspected.

## Slide 8
Dealing with Non Value Add
In our auto example, what can be done to eliminate the waste?

## Slide 9
Dealing with Non Value Add
In our auto example, what can be done to eliminate the waste?
The mechanic should not be getting the car, the car should come to the mechanic
The mechanic should have a full set of tools at arms length.
The car or work order should come with the parts (it could also come with the appropriate tools if special tools are required or the mechanic doesn’t have a full set)
Another worker should make the rounds disposing of used items
Once the mechanic signals that the work is done, the car should be removed from the work station and another brought in. During the idle time tools can be put away. Special tools should be picked up at the same time the car is moved out.
What about the time spent while the oil drains. This is not value added time but perhaps might be necessary, though while under the car the mechanic could do an inspection of the car.

## Slide 10
Learning To Identify Waste
The Lean Education Institute calls this “Learning to See”. Once you understand what waste is you can attack it. On the value stream map these areas are marked for a kaizan event.

## Slide 11
Setting Kanban Sizes
As we discussed earlier, a kanban is nothing more than a visual pull signal for something to be made. It is not totally unlike a reorder point in some cases, but it is certainly more visible.
There are various thoughts and kinds of kanbans. The simplest is a place on the floor, bin, or work surface that when empty needs to be filled. For instance, when our mechanic has an auto in his work area, it is pointless to put another one there since he cannot work on two at once. When the car leaves, the space is empty which should be a pull signal for another car to be placed in the work center. If you apply this to the factory, do not keep providing the next center material if they cannot process it. This may cause the previous center to stop work, but it certainly leaves a cleaner, more orderly plant and requires far less space.
Sometimes a two bin system is used, when one bin is empty it is sent back to the supplier while the other bin supplies material. The two bin system is easy, but not readily adjustable. It also has the danger of allowing too much inventory. If our bin sizes are large, we may get back a filled bin from the supplier before we have made a dent in the other bin.

## Slide 12
Setting Kanban Sizes
If we are not sure how big to make it (and we seldom are) we estimate the size and start there. We put the kanban card on the item that signals it is time to reorder, so when we get to that part, we send the card to the supplier. At that point there is a supply of the part left that should carry us until the stock is replenished. If there is too much left when the stock arrives we are carrying excess inventory. We can put another card in the supply to see if we ever reach it (in a rack it is typically a mark to see if inventory falls below that mark). If we do not, we can make the kanban smaller. We keep doing this until we are comfortable that our kanban size is correct.
This technique can also be used in the supermarket area.

## Slide 13
Mythical One Piece Flow
One piece flow is the ultimate goal in any company trying to get lean. One piece flow ensures quality, because each step in the process validates the previous one.
Large batches can contain flaws that are not recognized until they are used at which time large quantities may have to be reworked, or worse scrapped. Large batches also increase the total product cycle time.
Let us assume we have 5 steps each 10 minutes in length. We also are going to build 6 units.

## Slide 14
Mythical One Piece Flow
Op 1
Op 2
Op 3
Op 4
Op 5
When batches move through the system, it takes 60 minutes to go through each operation. If there is no move time, it takes 60 minutes before the second operation begins work. After 5 hours we can finally deliver parts.
60 min
60 min
60 min
60 min
60 min
300 min

## Slide 15
Mythical One Piece Flow
Op 1
Op 2
Op 3
Op 4
Op 5
With one piece flow the first unit comes out after 50 minutes and every 10 minutes thereafter we get another part. It takes 100 minutes to receive the last item.
10 min
10 min
10 min
10 min
10 min
50 min

## Slide 16
What Prevents One Piece Flow
While it is clear that one piece flow can yield great benefits, it is not always possible. Furnace operations, injection molding, deburring, etc. are cases where one piece flow does not make sense. Where goods cannot flow, kanbans and supermarket concepts should be used.

## Slide 17
Every Part Every Interval
Takt time is the rate at which the company receives orders. Producing at a higher rate than demand is wasteful. The goal is not only to match the rate of demand, but also match the mix.
If demand runs at the ratio 100 part A, 100 part B, 75 part C and 50 part D we need to produce at the rate of 4 As and Bs, 3 Cs and 2 Ds. In a truly flexible line, we might run production in this sequence
ABCABCDABDABC
The length of time to produce this set of parts in called an interval. We expect every part to be made in every interval at the rate of demand. We can monitor the progress of the plant by making sure that we do produce what is expected at the end of each interval.

## Slide 18
Quality
Lean companies are more likely to produce quality items. As already mentioned, flowing production ensures quality is checked at each step of the way. Engineering is also tasked to design to build. That is design the product so that it is easy to build (and thus to maintain) and that it is fool proof (poka yoke). Poka yoke ensures parts are put together properly by having them fit together only when properly oriented. A USB plug is an example. When we switched to from leaded to unleaded gasoline, cars requiring unleaded fuel had smaller openings so that leaded fuel hoses would not fit in them.

## Slide 19
Obsolescence
Change is a fact of life. To minimize the effect of change, keeping inventories lean lets a lean company to react faster to change with less inventory at risk.

## Slide 20
Other Tidbits
Machines wait for people, people don’t wait for machines. Waiting is wasteful.
Do not hide waste, identify it and try to eliminate it. Hidden waste will not be eliminated.
Simple is better than complicated. Single use machines require less set up, are less expensive and can react faster to changes in mix or volume.